## Slide 1
Kongsberg Maritime
ExxonMobil
Hammerhead Flexible Riser Slug Fatigue Study

## Slide 2: Slug Fatigue - Scope
Slugging mixture density series data will be provided for different longitudinal locations of the riser.
6 flow scenarios
Global analysis of 6 flow scenarios. A 3-hour simulation will be run to find the hot spots for further local fatigue analysis.
A local BFLEX model will be developed to calculate the tension and curvature to stress transfer functions
Flexstress is used to determine the stress time series from the curvature time series and calculate fatigue damage for each flow scenario.

## Slide 3: Slug Global Analysis – Input required
Global Analysis
Insert txt to Orcaflex
Run Simulation
Orcaflex model of the riser configuration
Flexible riser cross section data
SN curve
Slug input:
  - time
  - arc length
  - mixture density
  - flow rate
  - avg slug front velocity
Flow rate can be calculated according to:
Where is the fluid density, is the fluid velocity and is the internal area of the pipe

## Slide 4: Slug data
OLGA profile plot data files contains for every second:
  ROG (gas density)
  ROL (liquid density)
  HOLEXP (liquid holdup fraction)
  USFEXP (slug front velocities at section boundaries)
Mixture density can be calculated as:
  ROM=ROG*(gas holdup fraction) +ROL*HOLEXP
Flux volume velocity was used as input to Orcaflex

## Slide 5: Riser Configuration and Annulus Conditions
Orcaflex model was adjusted to match OLGA
Operational pressure profile for local fatigue analysis provided by ExxonMobil
    Conservatively used the highest pressure at hot spots
SN curve 1bar CO2
Annulus condition:
    Intact and dry (in air)
    Intact and wet
    Outer sheath damage/flooded and wet

## Slide 6: Riser Configuration – Orcaflex model
Adjustments made to the Orcaflex riser configuration to match the OLGA profile:
    Removed 10m riser length from the upper catenary
    Added 3m to the lower catenary
    Added static riser length on the seabed up to the drill center
    Added seabed slope according the excel sheet “FR-Jan2025-HH2-PR3”
  Other adjustments:
    Drag coefficient, changed from 1.8 to 0.7
    Structural damping 1.5% added
    Change mesh to 0.25m at TDP

## Slide 7: Riser Configuration – Orcaflex model
Chart: Seabed elevation
| 309.8 | 391.57743907318002 | 473.26998364365983 | 554.99735717559975 | 636.77059928955009 | 718.48746502093013 | 800.25691112631989 | 882.00161964226004 | 963.71163067363 | 1045.4660016242699 | 1127.2283583772798 | 1209.0178869991998 | 1290.77694843924 | 1372.54265258445 | 1454.27505559614 | 1536.0237656448098 | 1617.75965210103 | 1699.4823376950098 | 1778.2252590000001 | 1860.05067791837 | 1941.83467065221 | 2023.5889027195299 | 2105.2955348813202 | 2187.0145162087802 | 2268.7611768306151 | 2350.5739389504261 | 2432.3358851429384 | 2514.1384174407094 | 2595.8282097589772 | 2677.4827249114182 | 2759.2113664871749 | 2840.984304066048 | 2922.7222700275383 | 3004.5114290188772 | 3086.3061813744062 | 3168.0736513840052 | 3249.8521500000002
 | -1015.6116 | -1013.1347 | -1008.6603 | -1004.8757 | -1002.2637 | -998.2586 | -995.5303 | -992.1407 | -987.9981 | -984.8501 | -981.9171 | -979.9286 | -976.905 | -974.0668 | -970.3924 | -967.1007 | -963.5046 | -959.62 | -956.2422 | -953.6091 | -949.8993 | -945.5831 | -940.4438 | -935.5049 | -931.0475 | -928.0388 | -923.8712 | -920.5958 | -915.1955 | -909.2851 | -904.5087 | -900.5627 | -895.9486 | -892.3546 | -888.8902 | -884.8325 | -881.0035
More detailed view of the seabed slope
FPSO
Water depth:
1015.61m
Water depth:
881m
Distance TDP to Drill center: 2940m
Distance hang-off to TDP: 280m
Drill center
Water depth [m]

## Slide 8: Slug Fatigue Analysis
Premise:
  6 flow conditions were analyzed
  Intact and flooded annulus condition
  Hysteretic bending stiffness considering flooded and intact annulus is considered for the global analysis (one-to-one with local analysis).
  Pressure profile is provided for each bin. Max operating pressure out of all the bins in the TDP, buoyancy and hang off sections are chosen for the analysis.
  Total flux volume velocity is used in Orcaflex.
  KM is using the Tabular contents feature available in Orcaflex 11.4
Pressures used in Local Analysis | 
TDP | 14.69
HOG/SAG | 14.14
Bend Stiff | 5.10

## Slide 9: Conservatism in the Pressure Selection
  Internal pressure increases the friction stress in the pipe and hence by choosing the max pressure and applying that for all the bins is a conservative approach.
  Three fatigue dominant flow conditions (see table below) have lower operating pressures compared to max pressure. Using correct pressure for the respective bins would increase the fatigue life.
Pressures used in Local Analysis | 
TDP | 14.69
HOG/SAG | 14.14
Bend Stiff | 5.10
Bin | Internal Pressure |  | Individual Damage per Year 1) |  | Individual Fatigue Life (SF=10) | 
 | Actual Pressure | Used Pressure | Intact | Flooded | Intact | Flooded
HH2-PR3-LS-B2-SY04-L43-G07-Detail (Bin 2 Mid) | 11.5 | 14.69 | 1.13E-03 | 3.93E-04 | 88 | 255
HH2-PR3-LS-B4-SY25-L20-G01-NC-Detail (Bin 4-Test NC) | 9.9 |  | 5.84E-03 | 1.95E-05 | 17 | 5124
HH2-PR3-LS-B4-SY25-L20-G17-Detail (Bin 4-Test GL) | 6.9 |  | 6.16E-03 | 9.33E-04 | 16 | 107

## Slide 10: Slug Fatigue Analysis
Local cross-sections are modelled in Bflex. Friction coefficient of 0.15 is used across all the layers in Bflex model.
Hysteresis models and Stress transfer functions are generated in Bflex.

## Slide 11: Slug Fatigue Analysis
From global fatigue analysis TDP region is identified as fatigue hotspot.

## Slide 12: Slugging Results – Damage per bin
Assume 1bar CO2 SN curve
Highest fatigue damage rates:
    Bin 2-Mid: Start Year 4
    Bin 4-Test NC: Non-choking case with terrain slugging
    Bin 4-Test GL: Gas injected to mitigate severe terrain slugging
Note that: 1) Individual fatigue damage is with 100% probability at individual arc length hot spot. 2) The combined fatigue damage/life includes the probability for each bin and arc length hot spot is determined by combining all the relevant bins.

## Slide 13: Global TDP Slugging Response
Bin 1 Early Life: Hydrodynamic slugging
Low fatigue life
Note that global curvature responses are with flooded global hysteresis

## Slide 14: Global TDP Slugging Response
Bin 2 Mid Life: Hydrodynamic slugging
Low fatigue life
Note that global curvature responses are with flooded global hysteresis

## Slide 15: Global TDP Slugging Response
Bin 4 Test NC: Terrain slugging
Low fatigue life
  One slug during 6.4 hours.
Note that global curvature responses are with flooded global hysteresis

## Slide 16: Global TDP Slugging Response
Bin 4 Test NC: Terrain slugging
Vertical movement of SAG is 20m
SAG clearance ranges from 27m to peak at 41m

## Slide 17: Global TDP Slugging Response
Bin 4 Test: Terrain slugging
Low fatigue life
  Two slugs during 3 hours.
Note that global curvature responses are with flooded global hysteresis

## Slide 18: Global TDP Slugging Response
Bin 4 Test GL: Hydrodynamic slugging
Low fatigue life
Note that global curvature responses are with flooded global hysteresis

## Slide 19: Global TDP Slugging Response
Bin 5 Test LR: Terrain slugging
High fatigue life
Slightly lower fatigue life is found in TDP versus SAG/hot spot for curvature/mixture density
Note that global curvature responses are with flooded global hysteresis

## Slide 20: Slug Fatigue Analysis - Results
Fatigue results for Flooded Annulus Condition (SN curve 1bar CO2)
Note that: 1) Individual fatigue damage is with 100% probability at individual arc length hot spot. 2) The combined fatigue damage/life includes the probability for each bin and arc length hot spot is determined by combining all the relevant bins.
Flooded Global and Flooded Local, with 1bar CO2 SN curve

## Slide 21: Slug Fatigue Analysis - Results
Fatigue results for Intact Annulus Condition (SN curve 1bar CO2)
Note that: 1) Individual fatigue damage is with 100% probability at individual arc length hot spot. 2) The combined fatigue damage/life includes the probability for each bin and arc length hot spot is determined by combining all the relevant bins.
Intact Global and Intact Local, with 1bar CO2 SN curve

## Slide 22: Slug Fatigue Analysis - Results
Fatigue results for Intact Annulus Condition (SN curve 1bar CO2)

## Slide 23: Slug Fatigue Analysis - Results
Fatigue results for Intact and Dry Annulus Condition (SN curve in air)
Note that: 1) Individual fatigue damage is with 100% probability at individual arc length hot spot. 2) The combined fatigue damage/life includes the probability for each bin and arc length hot spot is determined by combining all the relevant bins.
Intact Global and Intact Local, with Marintek In Air SN Curve
Intact Global and Intact Local, with 1bar CO2 SN curve

## Slide 24: Slugging heatmaps
No Slug
Slugging heatmaps
1-Early
2-Mid

## Slide 25: Slugging heatmaps
No Slug
Slugging heatmaps
4-Test NC
4-Test

## Slide 26: Slugging heatmaps
No Slug
Slugging heatmaps
4-Test GL
5-Test LR

## Slide 27
Riser | Bin | OrcaFlex Input for Mixture Density & Flow Velocity – Averaged over Time
PR3 | 1- Early | 
PR3 | 2- Mid | 
PR3 | 4- Test NC | 
No Slug

## Slide 28
Riser | Bin | OFX Input for Mixture Density & Flow Velocity
PR3 | 4- Test | 
PR3 | 4- Test GL | 
PR3 | 5- Test LR | 
No Slug